## Slide 1: Dynamics and Control
Control Seminar 1

## Slide 2: General RECAP – Session 1
Why do we need control systems?
Why is it important to be able to predict how a system behaves?

## Slide 3: Lecture recap:
Why do we model control?
  Understanding behaviour of controlled systems
  Tuning for optimum performance (speed, efficiency, rapid response)
  Preventing out-of control behaviour (resonance, oscillation, run-away)

## Slide 4: Method of operation for centrifugal governor
Video: https://www.youtube.com/watch?v=OG1AiaNTT6s
Drive from engine to governor
Engine
Control valve adjusts supply of steam to engine as linkage is moved by governor
Steam supply from boiler
As speed increases, flymasses rise and operate linkage
Angular velocity of governor shaft is proportional to engine rpm

## Slide 5: Systems and block diagrams
Open-Loop system
Closed-Loop (feedback) system
Plant or process
Input
Output
Plant and controller
Input
(desired result)
Output
(controlled)

## Slide 6: Representation of control systems
The block diagram for an element is drawn as follows:
The transfer function is thus given by:
Where is known as the characteristic function, and is the characteristic equation.
=

## Slide 7
Representation of Control Systems
Output
Input
+
_
Disturbance
Input Elements
Controller
Plant or Process
Disturbance Elements
Feedback Elements
+
+
error
A typical system has a block diagram of the following form
Each box will then contain the transfer function of the element contained in the box.

## Slide 8: Laplace Transforms
All based on the insight that any time dependent function can be written as
https://www.youtube.com/watch?v=3gjJDuCAEQQ
https://www.youtube.com/watch?v=n2y7n6jw5d0

## Slide 9: Laplace Transforms
Differentiate: multiply by s:
https://www.youtube.com/watch?v=3gjJDuCAEQQ
Integrate: divide by s:
https://www.youtube.com/watch?v=n2y7n6jw5d0

## Slide 10
Laplace Transforms: Linear functions
i) Addition and Subtraction (superposition applies)
ii) Multiplication by a constant
iii) Final Value Theorem
This theorem is only valid if the final value is finite and constant.
A table of Laplace transform pairs will be provided (also at the exam).
MMME2046 Dynamics and Control Lecture 1

## Slide 11
Table of Laplace Transforms
1 |  | 
2 |  | 
3 |  | 
4 | Unit impulse at t=0 | 1
5 | Unit step at t=0 | 
6 | Unit ramp | 
7 |  | 
8 |  | 
9 |  | 
1 |  | 
2 |  | 
3 |  | 
4 |  | 1
5 | Unit step at t=0 | 
6 |  | 
7 |  | 
8 |  | 
9 |  | 

## Slide 12
Table of Laplace Transforms (continued)
This Table will be provided in the exam handout.
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
15 |  | 
16 |  | 
 | where | 
10 |  | 
11 |  | 
12 |  | 
13 |  | 
14 |  | 
15 |  | 
16 |  | 

## Slide 13: lapLace Transforms Revision
Example 2 from Example sheet 0
a) Use Laplace transforms to determine the solution to the following differential equation in the time domain (i.e. )
Where is a unit step and the initial conditions are taken to be zero
b) Determine the transfer function of the system analysed in (a) taking to be the input and to be the output of the system.

## Slide 14: Part (a)
Step 1: transform the differential equation from the time domain to the s domain:
Becomes:
F(s) is (Unit step from the table of Laplace transforms)
So:

## Slide 15: Part (a)
Back to table of Laplace transforms (entry 17 in the table, page 11)

## Slide 16: Part (B)
To get the transfer function:
Rearrange so that:

## Slide 17: And this is the system response:

## Slide 18
Modelling of Simple Components
Lever Systems
Rotor with Viscous Drag
Mass-Spring-Damper System (Exercise)
Hydraulic Ram

## Slide 19
M
K
C
xi
xo
d) Spring-Mass-Damper System
Exercise: Noting that the input to the above system is a displacement, show that the transfer function for the system is given by
where

## Slide 20: How to – Example Sheet 1, no. 2
Derive expressions for the transfer functions that relate input torque and output angular displacement of the torsional system shown for the following cases:
The block has negligible mass
The block has a moment of inertia
Note that the torsional stiffness of the mass-less bar is k and the directions of T and θ are similar, as shown in the figure.
T
θ
Clamp

## Slide 21: Always think about the physics!
Case 1: The block has negligible mass
Time domain: Torque T causes bar to twist through an angle .
Laplace domain – remember that k is a scalar constant so
Transfer function:
T
θ
Clamp

## Slide 22: Case 2: Block has moment of inertia
Equation of motion: input torque causes block to move
Laplace domain
T
θ
Clamp

## Slide 23: Bonus: What does this mean?
Impulse response (wind up the clock and start the pendulum):
Inverse Laplace transforms give:
where

## Slide 24: Bonus: What does this mean?
Harrison’s chronometer – rotary pendulum not affected by the motion of the ship – solved the longitude problem.
My ancestors made these things (Ritchie of Methven)

## Slide 25: How to – Example Sheet 1, no. 2
Derive expressions for the transfer functions that relate input torque and output angular displacement of the torsional system shown for the following cases:
The block has negligible mass
The block has a moment of inertia
Note that the torsional stiffness of the mass-less bar is k and the directions of T and θ are similar, as shown in the figure.
T
θ
Clamp

## Slide 26: Important Take-AWAYS
Laplace transforms make solving differential equations much more straightforward.
Control modelling is about stability: the denominator of the transfer function tells you a lot about the system behaviour (more later)