## Slide 1: Dynamics and Control
Control SEMINAR 2

## Slide 2: General Introduction – Session 2
Non-linearity and the operating point
1st order systems
Characterising the system response

## Slide 3: Non-Linearity and the operating point
Remember that the control system is maintaining the operating condition close to an optimum efficiency – only small variations from this will occur in practice.
  Speed up, slow down, no reversal of direction.
Non-linearities such as: backlash, coulomb friction, clearance, and saturation should not come into play around this point.
pressure drop
flow
operating range
“nominal” operating point

## Slide 4: Brilliant idea no. 2
Hydraulic Position Control
  Also known as servo-assistance
  Aeroplane flaps
  Car brakes
  Power steering (some cars)
  Tractors and JCBs!

## Slide 5
drain
drain
fluid in
spool valve
load
cylinder
piston
area, A
a
b
y
xo
xi
q
Hydraulic Position Control System
How it works
  Operator changes setting (xi)
  Piston is fulcrum – spool valve (y) translates
  Spool valve admits fluid into cylinder

## Slide 6
spool valve
a
b
y
xo
xi
q
Case Study: Hydraulic Position Control System
Xo
Xi
+
_
1/Ts
μ
We showed that the transfer function is:
with the block diagram
1st order system
OR

## Slide 7
+
_
Xo
Xi
b/(a+b)
a/(a+b)
feedback link
Y
1/As
K
Q
spool valve
piston
Hydraulic Position Control System: Overall Transfer Function
From the block diagram
rearranging
K/As
spool valve and piston

## Slide 8: Stability

## Slide 9
Introduction to Transient and Steady-State Responses
i) Is the System Stable?
ii) How Accurate is the System in Steady State?

## Slide 10: Oscillatory step response

## Slide 11
iii) How Quickly Does the System Reach a Steady State?

## Slide 12
Practical Measures of Transient Response
Maximum Overshoot as a percentage of step size.
Number of Oscillations before system settles to within a fixed percentage (5% say) of its steady state value.
Rise Time: The time taken for output to rise from 5% to 95% of step size.
Settling Time: The time taken for output to reach and remain within ±5% of steady state value.
Steady State Error

## Slide 13: 1st order systems
Characteristic transfer function:
Step response:
  (stable system!)

## Slide 14: Example Sheet 3 question 2
Figure Q2 illustrates a simple system for controlling the level of liquid in a tank with uniform cross-sectional area A. The error signal is derived by comparing the actual height with the desired level , and is fed to a controller which drives a variable speed pump such that the controlled volumetric inflow rate to the tank is given by:
where is the transfer function of the controller. In addition, there is an uncontrolled disturbance inflow to the tank given by . The tank outflow passes through a restriction with linearised flow resistance .
For the case when the controller is a proportional controller with gain , such that
Derive the overall transfer function relating to and and show that the system is first order;
pump
Transducer
qi
R
hi
h
h
Restrictor
qD
ε
+ -

## Slide 15: Stage 1
Dynamics for the tank – we need an expression for h:
In the time domain:
Volume of tank = Ah(t)
In the Laplace domain,
pump
Transducer
qi
R
hi
h
h
Restrictor
qD
ε
+ -
Volume=Ah

## Slide 16: Stage 1
Transfer functions:
pump
Transducer
qi
R
hi
h
h
Restrictor
qD
ε
+ -
Volume=Ah

## Slide 17: Stage 2: Make the block diagram
pump
Transducer
qi
R
hi
h
h
Restrictor
qD
ε
+ -
Note: Transfer function derived previously describes relationship between Q and H – schematic shows that H is fed back to the summing junction

## Slide 18: Stage 3: Overall Transfer functions
(1)
(2)
Rearrange to give Transfer functions:
From (1):

## Slide 19: Stage 3: Overall Transfer functions
(1)
(2)
Rearrange to give Transfer functions:
From (2):

## Slide 20: Stage 3: Overall Transfer functions
For combined input and disturbance:
Have we shown that the system is first order?

## Slide 21: Example Sheet 3 question 2
Figure Q2 illustrates a simple system for controlling the level of liquid in a tank with uniform cross-sectional area A. The error signal is derived by comparing the actual height with the desired level , and is fed to a controller which drives a variable speed pump such that the controlled volumetric inflow rate to the tank is given by:
where is the transfer function of the controller. In addition, there is an uncontrolled disturbance inflow to the tank given by . The tank outflow passes through a restriction with linearised flow resistance .
For the case when the controller is a proportional controller with gain , such that
If the tank area and the flow resistance in consistent units, find the required value of the controller gain to give a system time constant of 5 seconds.
pump
Transducer
qi
R
hi
h
h
Restrictor
qD
ε
+ -

## Slide 22: Stage 3: Overall Transfer functions
For time constant, T, we must rearrange to give the form:

## Slide 23: Exam 2019 Question 4
Compulsory part
Written in a different style – it was set by colleagues at the Ningbo campus
Mathematically similar …

## Slide 24: Part 1

## Slide 25: Part 1
The question tells us that , so we can write the forward transfer function as
Error, E(s) is given by:
Using the blocks in the upper part of the diagram,

## Slide 26: Part 1
Multiply left and right by s+1:
Multiply both sides of the equation by s+5:
Rearrange to put terms in on the left and on the right:

## Slide 27: Part 1
The overall transfer function is therefore:

## Slide 28: Part ii
Part ii): A unit step input is given by: and using the transfer function from (i) the output is:
Using the final value theorem (remember to multiply by s!):
In the limit, s tends to zero so this becomes:

## Slide 29: Part iiI
There are two ways to do this:
The first is by following this reasoning: If the steady state error is within ten percent, then . So using the result from part (ii):
This holds true for K>9 and K<-11. We would normally only consider positive values for K so K>9 is an acceptable answer.

## Slide 30: Part iiI
The second method is more formal: Begin by defining the error as a function of s:
The error at steady state must be less than 10%, giving K>9

## Slide 31: Part iv
My first tip is not to get involved in the numerator of the transfer function. All the information you need is in the denominator – as a reminder, here are the relevant transforms from the table.

## Slide 32: Part iv
The denominator (remember its other name, the characteristic equation) of a closed loop second order transfer function has the form:
Where is the natural frequency and is the damping ratio.
From the answer to part (i):

## Slide 33: Part iv
So the unit (s0) terms give the natural frequency:
Terms in s give the damping ratio:
(from the question). and .
It follows that and K=6.2

## Slide 34: Part iv
K=6.2. To find :
Either:
and
Or , so .

## Slide 35: The End?
Any questions?