## Slide 1: Turbomachines – part 1 Introduction
Introduction to work in turbomachines from a flow perspective

## Slide 2: Content of this section
flow through rotor and stator cascades in compressors and turbines
aspects of axial flow machines
cascade flow passage design methods introduction for axial flow machines

## Slide 3
Axis direction of the machine
cr
c
cx
cm
c
Whittle’s jet engine, sectioned at University of Derby
c - absolute tangential velocity of the fluid
cx – absolute axial velocity of the fluid
cr – absolute radial velocity of the fluid
c – total absolute velocity of fluid
cm – absolute meridional velocity of the fluid
r
r
U = r, the azimuthal velocity of the blade at radius r, i.e. circumferential component.
Turbomachines


## Slide 4: Turbomachines have a natural axis
Define the directions by cylindrical coordinates with respect to the axis of the machine
X
Y
Z
r
X
Y
Z
r
Cylindrical, , r, z
 is the angle around the z axis with the Y axis as the zero angle; r is the length of the resultant; z is the component on Z direction
x
y
z
r
z

Cartesian, x, y, z
x is the length of the resultant in the x-direction etc.
x
y
z
Polar, r, , 
r is the length of the resultant,  is the angle made by r around the Z direction, and  is the angle made by r around the X direction.


With the Z axis aligned with the machine axis, the distance z along the axis, the rotation angle, , around the axis and r the distance radially from the axis, are all well defined for a rotating machine in cylindrical coordinates – not so well in Cartesian and polar.

## Slide 5: Flow direction in turbomachines
Total velocity – the velocity of the fluid at any point in the passage through the blades
Meridional velocity – the velocity in the plane defined by radial and axial velocity, and represents volume rate through the machine
Tangential velocity contains the energy imparted to the fluid
Swirl angle, also known as the tangential angle, between the tangential direction and the meridional direction, represents the ratio of power to volume flow delivered by the machine
Now we take the thermodynamic-fluid hybrid notation for velocity, c
Why c? Because we need to think Roman, celeritas is the Latin for speed.

## Slide 6: Velocities defining power and machine type
Meridional velocity, cm , defining machine type, i.e. how axial vs. tangential
Tangential velocity, c , defining power, i.e. how turned the flow is
X
Y
Z, axis direction
r
z

cm
X
Y
Z, axis direction
r
z

c
 is the swirl angle, i.e. how much turned the fluid is compared to its flow velocity through the machine.
c

## Slide 7: Relating thermodynamics to fluids in turbines and compressors
SFEE for a compressor stage
where h0 is stagnation enthalpy
which is a small modification from TF2 analysis
Moment of momentum, i.e. the torque due to tangential change
Work, i.e. rate of change of moment of momentum
In which the torque due to the fluid acting on the blades produces work as it makes the blades spin with tangential velocities U

## Slide 8: Inner peace…..the Euler work equation
Here we see the connection, at last, between fluid mechanics, dynamics, and thermodynamics. The energy principle matching the force movement principle, and the fluid driving the dynamic machine.
From thermodynamics
From fluid mechanics
From dynamics

## Slide 9: Example – Euler work
An axial turbine rotor speed is 12000 rpm, mean radius of the blade is 0.2 m, and the height of the blade is 0.01 m. Calculate the blade speed, U. Given the mass rate is 1 kg/s of air of density 0.8 kg/m3, calculate the axial velocity. Given tangential velocity changes from 200 m/s to 61 m/s, calculate the Euler work rate and hence, assuming air to be a perfect gas, with cp = 1.005 kJkg-1K-1, calculate the temperature change of the air.
[ans: 251 m/s, 99.5 m/s, 34.9 kW, -35C]

## Slide 10: Entropy
By the first and second law of thermodynamics, from TF2, we have:
And since dh = du + pdv +vdp, we have:
If there are no shear forces, i.e. no friction or mixing flow, then the process is isentropic, and Tds = 0, so that:
By SFEE, which on a streamline is dh + cdc + gdz = 0 (i.e. h+c2/2+gz=constant), with the expression for dh from above, it reduces to Bernoulli equation:
Stagnation pressure is constant if fluid is incompressible and there are only small pressure changes

## Slide 11: Rothalpy – ro(tational stagnation en)thalpy
Rewrite Euler work equation:
I is constant along streamlines through a turbomachine
By using static enthalpy, and relative velocity, w (i.e. [cA, cr, c-U]
Where h0,rel = h + ½w2
i.e. relative stagnation enthalpy is constant through blades provided the blade speed is constant

## Slide 12: How to get the rothalpy in terms of w
and
So
But
So
Now
Therefore:
So substituting into the expression for I:

## Slide 13: Fluids
Gases
Perfect gas obeys gas law and does not alter cp and cv when temperature changes.
Semi-perfect gas obeys gas law but cp and cv alter when temperature changes.
Steam
Turbomachines using steam operate close to the saturation line, or underneath it and so it is far from being a perfect gas.
Steam tables and charts are used to determine properties, according to the IAPWS, as detailed in the thermodynamic tables.

## Slide 14: Turbomachine material to cover
flow through rotor and stator cascades in compressors and turbines
aspects of axial flow machines
cascade flow passage design methods introduction for axial flow machines
factors for consideration in radial and mixed flow machines

## Slide 15
A flow in a turbine has cx = 50 m/s, swirl angle  = 30 and c = 97 m/s. Calculate cr and cm and c. [ans: 160 m/s, 168 m/s and 193 m/s]

## Slide 16: Turbomachinery part 2
Analysis of axial turbomachines

## Slide 17: Axial flow turbomachines
Description of blade profiles
Description of flow in cascades
general cascade flow characteristics
The flow through turbine cascades
The flow through compressor cascades
definition of important parameters for the design aspects of the flow and defining an initial design strategy for particular situations
A stage where the absolute velocity and direction at outlet and inlet are the same is called a normal stage

## Slide 18: Definition of compressor and turbine stage
A stage consists of a rotor and a stator
The rotor is responsible for work transfer
The stator is responsible for guiding the flow to the next rotor row
It is useful to consider the absolute velocity angles and the relative velocity angles
The former defines the work and the latter defines the flow relative to the aerofoils of the row
In a turbine stage, the order is stator (commonly called nozzle) row followed by rotor
In a compressor stage, the order is rotor row followed by stator row

## Slide 19
https://www.youtube.com/watch?v=Il27VvHu-s0

## Slide 20: 2D velocity analysis – axial flow simplification
This is a compressor stage – rotor in front of a stator
Meridional velocity is axial velocity since no radial velocity assumed i.e. cm = cx;
 is the swirl angle (verify by inspection it is tan-1(c/cx). It is the absolute velocity angle.
All velocities are resolved axially or circumferentially
Note: c indicates absolute velocity, w indicates relative to the blade speed velocity.
Therefore, w indicates the angle of attack of the flow approaching the blade, whereas c indicates how much the flow is turned by the stage which is related to work by the Euler work equation.
The azimuthal (circumferential) velocity can be divided into the component of the absolute and of the relative velocity vectors, which add up to the blade velocity.
w1
c1
U
w2
U
c2
c3
There is no relative velocity on the stator – it is stationary, it sees c2 absolute approaching it and c3 absolute leaves it, note in this case the obvious slip of the c3 velocity, i.e. the angle of the vector is not the same as the trailing edge angle
Rotor
Stator
Reference direction
1
1
2
2
3
w1
c1
c1
cx1
Swirl angle, 
Relative velocity angle, 

## Slide 21: Blade profile
l
Reference direction
Chord line

In this case, a compressor blade is shown, hence there are relative velocity (w) and velocity angles ()
Stagger angle: , between chord and reference direction
Space-chord ratio: s/l
Camber angle: 
Blade inlet angle: 1’, camber line to chord line
Blade outlet angle: 2’, camber line to chord line
s
w1
1’
1

Camber line
w2
2
2’

## Slide 22: Work for the stage
The angle of incidence is i = 1 - 1’, and the angle of deviation is  = 2 - 2’. The exit flow angle 2 is a critical performance parameter. The Euler work formula shows:
and c = c sin . Therefore, for axial flow turbomachine stages, with U constant, the exit angle of the absolute velocity determines the work.
Blade design is done commonly using computational techniques with prescribed velocity requirements on the surface of the blade. It is useful to consider traditionally prescribed geometries.

## Slide 23: Compressor row design
Overview design considerations of compressor blade design
  NACA 65 aerofoil series is commonly used – useful camber shape
  Maximum thickness is only 5-10% of chord, at 40% chord position
  Rounded leading-edge designs are suitable for wider range of approach velocity and therefore of speed, but has poor high-speed characteristics
  Sharper blades have the opposite effect
  Cannot overload a stage or large pressure losses occur, therefore use the de Haller limit:
Chart: NACA65-210
| 1 | 0.95013999999999998 | 0.90027999999999997 | 0.85038000000000002 | 0.80044000000000004 | 0.75044999999999995 | 0.70043 | 0.65036000000000005 | 0.60026999999999997 | 0.55013999999999996 | 0.5 | 0.44984000000000002 | 0.39967999999999998 | 0.34950999999999999 | 0.29936000000000001 | 0.24920999999999999 | 0.19908999999999999 | 0.14899000000000001 | 9.894E-2 | 7.3940000000000006E-2 | 4.8980000000000003E-2 | 2.4080000000000001E-2 | 1.1690000000000001E-2 | 6.7799999999999996E-3 | 4.3499999999999997E-3 | 0 | 5.6499999999999996E-3 | 8.2199999999999999E-3 | 1.3310000000000001E-2 | 2.5919999999999999E-2 | 5.1020000000000003E-2 | 7.6060000000000003E-2 | 0.10106 | 0.15101000000000001 | 0.20091000000000001 | 0.25079000000000001 | 0.30064000000000002 | 0.35049000000000002 | 0.40032000000000001 | 0.45016 | 0.5 | 0.54986000000000002 | 0.59972999999999999 | 0.64964 | 0.69957000000000003 | 0.74955000000000005 | 0.79956000000000005 | 0.84962000000000004 | 0.89971999999999996 | 0.94986000000000004 | 1
 | 0 | 0.00622 | 0.01327 | 0.02057 | 0.02783 | 0.03479 | 0.04128 | 0.04712 | 0.05217 | 0.05625 | 0.05915 | 0.06058 | 0.06067 | 0.05954 | 0.05732 | 0.05397 | 0.04938 | 0.04338 | 0.03555 | 0.03069 | 0.02491 | 0.01757 | 0.01273 | 0.00999 | 0.00819 | 0
 | 0 | -0.00719 | -0.00859 | -0.01059 | -0.01385 | -0.01859 | -0.02221 | -0.02521 | -0.02992 | -0.03346 | -0.03607 | -0.03788 | -0.03894 | -0.03925 | -0.03868 | -0.03709 | -0.03435 | -0.03075 | -0.02652 | -0.02184 | -0.01689 | -0.01191 | -0.00711 | -0.00293 | 0.0001 | 0

## Slide 24: Compressor row design
  Approximate indication of deviation angle is by Carter’s rule:
  In which  is camber angle, a is distance from leading edge to thickest part of aerofoil, n is 0.5, s is circumferential blade spacing,  is swirl angle out of rotor row.
  Incidence angle can be positive (steeper angle of attack, separation risk), neutral (design angle of attack) or negative (will produce flow leakage from suction side to pressure side and hence worse deviation)
  Suction side is accelerated flow and therefore influenced by M
  Density change from inlet to outlet is the axial velocity density ratio (AVDR) – gets bigger as density increases
a
Max camber
Suction side
Pressure side
-ve
+ve

## Slide 25: A compressor drags the flow
The paddle pulls on the water and leaves an unstable wake

## Slide 26: Turbine row design
Overview design considerations of turbine blade design
  Boundary layer is much more stable than compressor because the flow is accelerating, and pressure is falling
  each stage can have a much higher loading without flow separation
  the flow deflection can be greater than 120
  the ratio of c2/c1 can be between 2 and 4
  Losses rapidly rise as approaching and exceeding M=1 – trailing shock waves produce significant drag
  M=1 is the limiting load, since no higher flow rate can be achieved by increasing the Mach number

## Slide 27
https://www.youtube.com/watch?v=sd7uHUxdoOw

## Slide 28: Axial turbine design - Zweifel criterion (for incompressible) interpretation – determines optimum s/l
As  increases, tan  tends to increase to infinity at 90 and cos  tends to decrease from 1 at zero to 0 at 90, b is axial length of chord
1
1
2
2
b
Nozzle row (stationary)
Rotor row (rotating)
3
c1
c1
c2
c2
c3
c3
3
w3
w3
w2
w2
U
U
Axial chord
s
Blade spacing
b
s

## Slide 29
Example: For a turbine rotor row with inlet velocity c1 at 70 and outlet c2 at 20, use the Zweifel criterion for the blade spacing and determine the blade spacing for turbine blades with chord 40 mm and stagger angle 25.
[ans: 0.14, 6.2 mm]

## Slide 30: Mean line design of gas turbines – incompressible flow assumed
A starting design of an axial turbine stage is done using the following method. Design enhancement is then by computational methods.
Three design parameters:
Flow coefficient, the through-flow compared to the radial speed:
Stage loading, the change in tangential velocity, or work:
Stage reaction, the work of pressure vs. flow:

## Slide 31
2
c2
w2
U
3
c3
w3
U

## Slide 32: The repeating or normal stage
A repeating stage is convenient for high power applications with many stages
In a repeating stage, the velocity triangles repeat after each stage
Thus, cx is constant (by altering the cross-sectional area of the annular gap through which flow proceeds), rmean of the blades is constant, absolute velocity angle, , is the same at entry and exit of the stage
The following relationships are consequent on this set of conditions:
From which blade angles can be estimated (these can also be expressed in terms of )

## Slide 33: Mean line design of gas turbines
Number of stages:
Blade height and mean radius of blade:
Number of aerofoils and chord, for use with Zweifel criterion to get s
There will be high values of blade height in low pressure stages

## Slide 34: GEC Alstom IP steam turbine – blade height and mean radius changes

## Slide 35: GEC Alstom LP steam turbine – large blade height

## Slide 36: Turbine blades significant twist when radius change increases

## Slide 37: Stage reaction combined velocity triangles
w2 (= w3)
c2
c3
w3
Zero reaction stage rotor:
no axial velocity change,
It can be shown that (relative velocity angles) 2 = 3
Therefore (relative velocities) w2 = w3
Advantage: high stage loading
Disadvantage: chance of separation – highly cambered blades
Use: some steam turbines
Entry
Exit
U
U
2 = 3
50% reaction stage rotor:
Symmetrical velocity triangles
Similar stator and rotor blade shapes, high acceleration and
lower turning and hence lower losses
Advantage: subsonic Mach numbers
Disadvantage: increased number of stages required
Use: gas turbines and some steam turbines
w2
c2
c3
w3
Entry
Exit
2
3
3
cx

## Slide 38: Proving the points
For the repeating stage, zero reaction:
i.e.
For the repeating stage, 50% reaction:
Trigonometry: and and
Therefore:
And therefore,
(Inverted flow coefficient)

## Slide 39: Design process
Given a particular flow coefficient, stage loading coefficient, and reaction, the blade angles can be determined, the mean radius and velocity in the channel can be related, and conditions of the fluid at each point can be determined.
solve for tan  terms:
Now we can use these in an example
Slide 30,

## Slide 40: Design of turbine stage using parameters
Example: A turbine stage has a desired flow coefficient of 0.8, reaction of zero and stage loading of 5.1. Find the entry and exit relative flow angles and sketch the velocity triangles; calculate the axial velocity and given that the blade speed is 100 m/s, calculate the swirl angles, . [ans: 72.6, see next slide, 80 m/s, 62.5, 77.3]

## Slide 42
Example: Given the blades in the previous question are at a mean radius of 0.15m and that the blade height is 0.01m, and that the static pressure and temperature at nozzle exit are 8 bar and 1600K and the gas is air with R = 287 J/kgK, calculate the mass flow rate. [ans 1.313 kg/s]